BACK TO PROPOSALS

Summary
paper

# Project Description
Objectives
1. Can a fabric be utilized in a flexible formwork to form a concrete member in a manner that has certain distinct advantages over the currently predominant method of forming concrete with a rigid formwork?
2. Can efficiencies using a flexible formwork be realized significantly enough to reduce our impact on the built environment in terms of materials and energy usage – is it sustainable?
3. Can a flexible fabric formwork be used to design concrete members in a manner that would be practical and useful to the design community?
Goals

efficient and sustainable
Background
Concrete International

Array

sustainable
## Proposed Research
Phases I and II
distinct
Phase III
- sustainable
### Phase I – Proof of Concept
– Fabric as a Load Carrying Component
PhotoModeler 6

Array
Array
Array
Array
reused
ADINA

1. Phase I – Test Series 1
  1. Panel size – 24 inches x 36 inches x 6 inches thick (609.6 mm x 914.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels stretched to just a taut state
  3. Water loading
  4. Measurements taken
    1. deflection at geometric center
    2. fabric strain at selected locations
    3. load cell at each corner of test frame
  5. Panels loaded and unloaded for three (3) cycles
2. Phase I – Test Series 2
  1. Panel size – 24 inches x 36 inches x 6 inches thick (609.6 mm x 914.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels prestressed 1% in the 24 inch (609.6 mm) machine direction (warp) and just taut in the 36 inch (914.4 mm) cross machine direction (fill)
  3. Water loading
  4. Measurements taken
    1. initial prestress in fabric
    2. deflection at geometric center
    3. fabric strain at selected locations
    4. load cell at each corner of test frame
  5. Panels loaded and unloaded for three (3) cycles
3. Phase I – Test Series 3
  1. Panel size – 24 inches x 36 inches x 6 inches thick (609.6 mm x 914.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels prestressed 1.5% in the 24 inch (609.6 mm) machine direction (warp) and just taut in the 36 inch (914.4 mm) cross machine direction (fill)
  3. Water loading
  4. Measurements taken
    1. initial prestress in fabric
    2. deflection at geometric center
    3. fabric strain at selected locations
    4. load cell at each corner of test frame
    5. Panels loaded and unloaded for three (3) cycles
4. Phase I – Test Series 4
  1. Panel size – 24 inches x 36 inches x 6 inches thick (609.6 mm x 914.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels prestressed 2% in the 24 inch (609.6 mm) machine direction (warp) and just taut in the 36 inch (914.4 mm) cross machine direction (fill)
  3. Water loading
  4. Measurements taken
    1. initial prestress in fabric
    2. deflection at geometric center
    3. fabric strain at selected locations
    4. load cell at each corner of test frame
    5. Panels loaded and unloaded for three (3) cycles
### Phase II – Proof of Concept
– Fabric as a Concrete Load Carrying Component
cleaned and reused
ADINA

1. Phase II – Test Series 1
  1. Panel size – 36 inches x 48 inches x 6 inches thick (914.4 mm x 1,219.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels stretched to just a taut state
  3. Plain concrete loading
  4. Measurements taken
    1. deflection at selected locations
    2. fabric strain at selected locations
    3. thermal couples in concrete
    4. load cell at each corner of test frame
  5. Panels loaded and unloaded (fabric stripped) for three (3) cycles
2. Phase II – Test Series 2
  1. Panel size – 36 inches x 48 inches x 6 inches thick (914.4 mm x 1,219.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels prestressed 1% in the 36 inch (914.4 mm) machine direction (warp) and just taut in the 48 inch (1,219.4 mm) cross machine direction (fill)
  3. Plain concrete loading
  4. Measurements taken
    1. initial prestress in fabric
    2. deflection at selected locations
    3. fabric strain at selected locations
    4. thermal couples in concrete
    5. load cell at each corner of test frame
  5. load cell at each corner of test frame
  6. Panels loaded and unloaded (fabric stripped) for three (3) cycles
3. Phase II – Test Series 3
  1. Panel size – 36 inches x 48 inches x 6 inches thick (914.4 mm x 1,219.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels prestressed 1.5% in the 36 inch (914.4 mm) machine direction (warp) and just taut in the 48 inch (1,219.4 mm) cross machine direction (fill)
  3. Plain concrete loading
  4. Measurements taken
    1. initial prestress in fabric
    2. deflection at selected locations
    3. fabric strain at selected locations
    4. thermal couples in concrete
    5. load cell at each corner of test frame
  5. Panels loaded and unloaded (fabric stripped) for three (3) cycles
4. Phase II – Test Series 4
  1. Panel size – 36 inches x 48 inches x 6 inches thick (914.4 mm x 1,219.4 mm x 152.4 mm thick)
  2. Six (6) fabric panels prestressed 2% in the 36 inch (914.4 mm) machine direction (warp) and just taut in the 48 inch (1,219.4 mm) cross machine direction (fill)
  3. Plain concrete loading
  4. Measurements taken
    1. initial prestress in fabric
    2. deflection at selected locations
    3. fabric strain at selected locations
    4. thermal couples in concrete
    5. load cell at each corner of test frame
  5. Panels loaded and unloaded (fabric stripped) for three (3) cycles
### Phase III – Proof of Concept
– Fabric Used to Form a Practical Load Carrying Component
ADINA
ADINA

Array
Array
1. Phase III – Test Series 1 (Control Panel)
  1. Panel size – 12’-0” x 8’-0” x 3½”-thick (3.7 m x 2.4 m x 88.9 mm thick)
  2. Six (6) fabric panels prestressed 2% in the 8’-0” (2.4m) machine direction (warp) and just taut in the 12’-0” (3.7 m) cross machine direction (fill), three (3) panels for positive loads and three (3) panels for negative loads
  3. Plain concrete mix
  4. Measurements taken during forming
    1. initial prestress in fabric
    2. deflection at selected locations
    3. thermal couples in concrete
    4. fabric strain at selected locations
    5. load cell at each corner of test frame
  5. Panels stripped from fabric and loaded laterally to simulate positive and negative wind loads (uniform load applied using vacuum chamber)
  6. Measurements taken during lateral loading
    1. deflection at selected locations
    2. concrete strain at selected locations
    3. load cell at panel reaction points
2. Phase III – Test Series 2 (Reinforced Panel)
  1. Panel size – 12’-0” x 8’-0” x 3½”-thick (3.7 m x 2.4 m x 88.9 mm thick)
  2. Six (6) fabric panels prestressed 2% in the 8’-0” (2.4 m) machine direction (warp) and just taut in the 12’-0” (3.7 m) cross machine direction (fill), three (3) panels for positive loads and three (3) panels for negative loads
  3. FRP or steel reinforced concrete panel
  4. Measurements taken during forming
    1. initial prestress in fabric
    2. deflection at selected locations
    3. thermal couples in concrete
    4. fabric strain at selected locations
    5. load cell at each corner of test frame
  5. Panels stripped from fabric and loaded laterally to simulate positive and negative wind loads (uniform load applied using vacuum chamber)
  6. Measurements taken during lateral loading
    1. deflection at selected locations
    2. concrete strain at selected locations
    3. load cell at panel reaction points

###
## See Also
Place text here.
## References
Concrete International
http://www.umanitoba.ca/cast_building/
Concrete International
PhotoModelerAvailable
ADINAAvailable
## External Links
Place links here.